## Slide 1: Image Processing for Microscopy
QCBio Collaboratory Workshop
Haripriya Vaidehi Narayanan
haripriyavn@ucla.edu
Nov 2022

## Slide 2
GOALS OF THIS WORKSHOP
  Understand how microscopy images are formed, what is a digital image, and how to work with it
  Understand basic mathematical principles of common operations performed on images and image sequences
  Develop a simple pipeline to quantitatively analyze objects in a given image
  Become able to use online resources to follow advanced topics confidently
  You WILL NOT become an expert in image processing BUT…
  You WILL gain the tools to go on a self-learning journey towards expertise! 😊

## Slide 3
WORKSHOP STRUCTURE & SYLLABUS
  Day 1 – Basic physics, math & computational principles of image processing
    Image formation, display, and storage
    Spatial resolution & bit depth
    Images as pixel intensity histograms
    Images as matrices
  Day 2 – Fundamentals of image processing pipeline development
    Image filtering
    Thresholding & segmentation
  Day 3 – Feature extraction, quantitative analyses, and object tracking
    Morphological operations
    Quantifying object properties
    Basics of object tracking

## Slide 4
COURSEWORK & GRADING POLICIES
  We will work entirely in this online Google Co-Lab notebook. This will be both your course “textbook” and “workbook”.
  Each day has a take-home quiz – open-book, open-notes, open-Google-search! Fill in and email me your answer sheets before 8.30AM next morning. (Day 3 = in-class quiz)
  You may NOT consult another student on the quiz questions, nor post your questions on stack-exchange, Quora, or any homework help sites.
  We will discuss the answers in class the next day. Minimum score in this course can be 50%!! For every question you get wrong, if you submit another answer sheet writing down WHY your answer was wrong, you will get half-credit!
  Grading is on an absolute scale. <40% = fail, 40-55% = D, 55-70% = C, 70-85% = B, >85% = A.

## Slide 5
WHY DO WE NEED IMAGE PROCESSING?
  After all, couldn’t we just do it all by hand?!
  Take a look at the following image of nuclei within a bunch of cells. Say, you want to get size & brightness of each nucleus, to determine if it’s dividing or not!
  Think about how you’d manually complete the tasks of –
  counting the number of nuclei,
  measuring the area of each nucleus, and
  measuring the corresponding brightness.
  Then consider a video where you’re trying to see how these parameters are changing over time.
  What challenges can you foresee in this task?

## Slide 6
WHY DO WE NEED IMAGE PROCESSING?
  Manual processing is highly variable, cumbersome, and time-consuming
  Images are now a form of multi-dimensional big data! We can collect terabytes (1TB = 1M MB) per experiment!!
  Hence, automation is required for consistency and throughput.
  The challenge of image processing is that each problem can be unique, requiring tailor-made pipelines depending on its particular features.
    Therefore, it’s important to understand the fundamental principles and use them contextually, rather than applying formulaic plug-and-play pipelines.

## Slide 7
line
WHY DO WE NEED IMAGE PROCESSING?
We need to know what’s available in the toolbox, and what the different tools do

## Slide 8
MANY TOOLS AVAILABLE FOR IMAGE PROCESSING
  There are numerous off-the-shelf tools which you MUST explore (on your own…)
  Here, we will learn what’s happening beneath the hood in the functions provided by these tools, so that you can choose which operations to use or parameters to tweak.
cellpose

## Slide 9
SOME MORE LEARNING RESOURCES (AMONG MANY OTHERS…)
  iBiology Bioimage Analysis Course: The Life Cycle of an Image Data Set – https://www.ibiology.org/online-biology-courses/bioimage-analysis-course/
  Introduction to Bioimage Analysis by Pete Bankhead – (my personal favourite) https://bioimagebook.github.io/README.html
  Bioimage analysis notebooks by Robert Haase – https://haesleinhuepf.github.io/BioImageAnalysisNotebooks/intro.html YouTube lectures - https://www.youtube.com/playlist?list=PL5ESQNfM5lc7SAMstEu082ivW4BDMvd0U
  FIJI YouTube tutorials – https://www.youtube.com/playlist?list=PL5Edc1v41fyCLFZbBCLo41zFO-_cXBfAb
  CellProfiler YouTube workshops – https://www.youtube.com/playlist?list=PLXSm9cHbSZBCfLa3KAgMcndCXQvJluEtF
  University of Geneva Bioimaging core : list of online courses / resources – https://www.unige.ch/medecine/bioimaging/en/information/tutorials-1/online-courses/

## Slide 10
PACKAGES USED IN THIS WORKSHOP
  Fiji for GUI : Download from Fiji.sc
  Python Co-lab for notebooks
  numpy for arrays
  matplotlib for plotting graphs & displaying images (image, pyplot)
  scikit-image for command line image analysis : Read the API documentation here
  scikit-image is structured as a set of sub-packages or modules, which must be individually imported to use in your pipeline. The main modules we’ll use are – * color * data * exposure * feature * filters
  * measure * morphology * transform * util
  Let us start by making sure we have all of these packages installed and working!

## Slide 11
HOW IS AN IMAGE FORMED AND DIGITIZED?

## Slide 12
SPATIAL RESOLUTION OF AN IMAGE
pixel
pixel
  Pixel size is a built-in physical property of the camera
  We cannot measure spatial structures smaller than a single pixel!
  Binning pixels reduces random noise at the expense of resolution

## Slide 13
POINT SPREAD FUNCTION
  Wave nature of light – a point source forms a diffraction pattern!
  Objective numerical aperture & light wavelength determine resolution
  Two spots must be (half Airy disk) distance apart to become resolvable
Zeiss Online Campus
Edinburgh Instruments
Teledyne Photometrics

## Slide 14
BIT-DEPTH OF AN IMAGE
  Number of levels for intensity resolution of an image
  Bit depth can be downsampled (although info is lost)
  Bit depth cannot be upsampled (needs interpolation)
Teledyne Lumenera
DIY Photography
Silkypix

## Slide 15
LOOK UP TABLES & IMAGE DISPLAY

## Slide 16
COMPRESSION, DATA STORAGE & FILE TYPES
  Imaging data has 2 components –
  The imaging data (pixel values)
  The metadata
    Pixels to micron conversion scale
    Dimensions
    Bit-depth
    Pixel size (physical dimensions of each pixel on camera)
    Objective properties …etc etc
  OME-TIFF format (Open Microscopy Environment) tries to standardize metadata

## Slide 17
COMPRESSION, DATA STORAGE & FILE TYPES
  Uncompressed data –
    Preserves all pixel values and metadata
    Only option for accurate quantitative analysis
    You MUST retain your raw uncompressed files until (& ideally also after) publication of your manuscript!
    Generally comes in proprietary file formats –
      CZI (Zeiss), ND2 (Nikon), LIF (Leica), OIB (Olympus)
      Can be opened by BioFormats plugins (Fiji, Napari for Python)
    Can be saved as TIFF files – best file type option for export and analysis

## Slide 18
COMPRESSION, DATA STORAGE & FILE TYPES
  Loss-less compression –
    Less reduction in file size
    However, all original data can be reconstructed ; very practical!!
    Good for display in publications, presentations, etc
    Commonly used file formats –
      * PNG * BMP * TIFF (LZW compression)
    When you get a TIFF file – Note that it could be compressed or not, and check before analyzing!!
    You can also make ZIP archives for lossless compression

## Slide 19
COMPRESSION, DATA STORAGE & FILE TYPES
  Lossy compression –
    More reduction in file size, but at the cost of data quality!
    Some original data may be permanently lost
    Commonly used file formats * JPEG * GIF
    Good for display in websites, thumbnails
    Otherwise, AVOID JPEG LIKE YOUR WORST ENEMY
    Once you compress a file with loss, you cannot re-save it in a different format and expect to regain the data – ”what is lost is forever gone”!!
    NEVER analyze lossy compressed files – pixel values cannot be trusted

## Slide 20
COMPRESSION, DATA STORAGE & FILE TYPES
  Image pyramid -
    Technique to speed up display across various zooms
    Used for full slide scans, region tiling, etc
    Stores multiple versions of the image at different spatial resolutions
Wikipedia

## Slide 21
COMPRESSION, DATA STORAGE & FILE TYPES
  How can we calculate file size of an image (sequence) in memory ?
    Bit depth = number of bits required to store 1 pixel
    Dimensions X * Y = total number of pixels in 1 image
    Channels = number of images in 1 composite frame
  Bit-depth * Dimensions * Channels * Frames = Total #bits required
  8 bits = 1 byte 1024 bytes = 1 kB (not 1000 bytes!)
  1024 kB = 1 MB
  1024 MB = 1 GB

## Slide 22
    RGB colour images – 3 brightness values per pixel : colour triplet [R, G, B]
    Camera needs to take 3 images (1 in each channel) and superimpose them
    Physical detector must be configured to collect an RGB colour image
    RGB to grayscale conversion – Vector addition : grayscale
    Triplet representation of grayscale – [K, K, K] Can you convert grayscale to RGB? Why or why not?
INCREASING DIMENSIONS : RGB COLOUR IMAGES

## Slide 23
INCREASING DIMENSIONS : VIDEO DATA
    Video data is simply a sequence of images separated by intervals of time
    Video data is 4D – X, Y, intensity, time (higher-D depending on # of channels)
    Frame rate – number of images collected per unit time
      Important for measuring dynamical information (eg. object speed)
    Playback speed – number of images displayed per unit time This can be anything you like – sped up or slowed down – which makes the phenomena in the video look interesting
    Video processing is often simply image processing for each frame
    Tracking : connecting objects across frames (we will look at this on Day 3)

## Slide 24
SIMPLE OPERATIONS ON VIDEO DATA
Temporal localization using sliding window
Flattening with Z-stack projection
Feeding currents of a Veliger snail larva.
Video credits : William Gilpin Flowtrace : Gilpin W, Prakash VN & Prakash M, JEB (2016).

## Slide 25
IMAGE HISTOGRAMS : STATISTICAL OPERATIONS
    Intensity values of an image can be represented as a frequency distribution
    Binned pixel value distribution – histogram of the image We can perform statistical operations on the pixel intensity histogram!

## Slide 26
    Binary images are a special case of grayscale with bit depth = 1
    Each pixel takes only values 0 or 1
    Can be interpreted as FALSE vs TRUE – Boolean logic i.e. Can apply AND, OR, NOT, NAND, XOR gates to/between binary images!
    Grayscale to binary conversion – Cutoff between 0 & 1 is called threshold
    Also called binary masks – can be used to isolate a specific part of an image
BINARY IMAGES : LOGICAL OPERATIONS
Put image here showing 8-bit vs 1-bit

## Slide 27
IMAGES AS MATRICES : POINT OPERATIONS
    Images are comprised of intensity values tied to spatial locations Scrambling example shows how important the spatial location is
    Mathematical representation of images = 2-D row-column matrix Hence, all matrix operations are possible!

## Slide 28
MATRIX TRANSFORMATIONS IN X-Y-Z
    Affine transformations – preserve collinearity of points along a line
      Scaling
      Translation
      Rotation
      Skew

## Slide 29
MATRIX TRANSFORMATIONS IN X-Y-Z
    Non-affine transformations – do not preserve collinearity of points
      Eg. Warping, sweeping along a path, projections

## Slide 30
IMAGE REGISTRATION
    Transforming image matrices to align on same absolute coordinate system
      Apply affine transforms through matrix multiplication
      Minimize distance between fiduciary markers
      Reverse engineer the transformations that differentiate the two images

## Slide 31
IMAGE FILTERING
    Filtering – applying a small matrix operation to each pixel of an image
      Small matrix = Kernel of the filter
      Application of the kernel = Convolution with the filter
    Filters enhance the features in an image and reduce noise Noise = random Gaussian variations in pixel intensity
    Linear filters – linear combination of pixels (Mean, Gaussian, etc)
    Non-linear filters – non-linear combinations of pixels (Rank & edge filters) Cannot recreate original image after non-linear filtering!! Always keep a copy of the original, and work on a duplicate image

## Slide 32
IMAGE FILTERING
    Mean filters –

## Slide 33
IMAGE FILTERING
    Rank filters –

## Slide 34
IMAGE FILTERING
    Sobel filters –
    Prewitt filters –
    Roberts cross operator –

## Slide 35
IMAGE FILTERING
    Gaussian filters & their derivatives –
Gaussian
Laplacian of Gaussian (LoG)

## Slide 36
THRESHOLDING & SEGMENTATION
    Recall – Thresholding creates binary images by deciding on a cutoff value
    Thresholding separates foreground from background of an image
      Global thresholding vs local thresholding
    Segmentation = separating individual objects in an image
    Automated segmentation avoids biases from manual segmentation
    The choice of threshold value is very important (but often not perfect!)
      Too high threshold = object size reduced, some objects lost
      Too low threshold = object size increased, some objects merged
    Different thresholding algorithms suit different histogram distributions

## Slide 37
THRESHOLDING & SEGMENTATION
    Recall – Thresholding creates binary images by deciding on a cutoff value
    Thresholding separates foreground from background of an image
      Global thresholding vs local thresholding
    Segmentation = separating individual objects in an image
    Here is some theory for four different thresholding algorithms –
      Mean thresholding – simple pixel average, you may get lucky!
      Minimum – best for bimodal histograms (may fail to converge!)
      Triangle – best for eliminating a dominant background with low signal
      Otsu – best for separating bimodal histogram with deep valley
Minimum
Triangle
Otsu

## Slide 38
MORPHOLOGICAL OPERATIONS
    Connected components – contiguous areas of bright pixels in binary image
      4-connected (1-connectivity) = top, bottom, and sides only
      8-connected (2-connectivity) = allows connection along diagonal neighbours
    Segmentation yields a binary mask with connected components
      Inaccuracies – components may either overlap or be broken up
      Morphological operations allow us to adjust connected components
    Structural element (strel) – “kernel” for morphological operations
1-connectivity 2-connectivity
[ ] [ ] [ ] [ ]
| \ | /
[ ]--[x]--[ ] [ ]--[x]--[ ]
| / | \
[ ] [ ] [ ] [ ]

## Slide 39
MORPHOLOGICAL OPERATIONS
    Structural element (strel) – “kernel” for morphological operations

## Slide 40
MORPHOLOGICAL OPERATIONS
    Erosion = min-filter with strel kernel, reduces bright areas
    Dilation = max-filter with strel-kernel, expands bright areas Erosion & dilation may preserve neither areas nor # of CCs
    Opening = Erosion then dilation (same strel), disconnects CCs
    Closing = Dilation then erosion (same strel), merges CCs Opening & closing approximately preserve areas while changing # of CCs
    Area opening / remove bright spots
    Area closing / fill small holes
    Edge finding – inner vs outer boundaries
    Convex hull & skeletonization

## Slide 41
FEATURE EXTRACTION & OBJECT PROPERTIES
    Each connected component is labeled with an index number
      Background gets the index 0
    Properties –
      Area
      Centroid
      Eccentricity
      Intensity_max, intensity_image
      Perimeter
      Solidity … etc etc

## Slide 42
SIMPLE INTRO TO OBJECT TRACKING